## Slide 1: CSIT 404 VOICE COMMUNICATION TECHNOLOGY
Session 1 – Introduction
Lecturer: Mr. Paul Nii Tackie Ammah, CSD
Contact Information: pntammah@gmail.com

## Slide 2: Session Overview
This session starts with the basics, how a telephone call is made. We describe some of the physical and logical components of the telephone system required for a telephone call to occur: the PBX, switch, telephone, trunk, subscriber, line, tie line, and Central Office (CO).
Next, it examines the different types of signaling exchanged between the components of the telephone system, also known as the Public Switched Telephone Network, PSTN.
At the end of the session every student should be able to
Describe how a phone call is made.
The basic analog phone system components - phones, PBX, trunks, lines, switches.
How phone system components communicate with each other using signaling.

## Slide 3: Session Outline
The key topics to be covered in the session are as follows:
Understanding the Phone System

## Slide 4: Understanding the Phone System
Topic One

## Slide 5: Making a Call
You pick up the phone, dial some digits, wait for the person you called to pick up their ringing phone, and then you begin your conversation.
What is beyond the phone and the phone outlet in the wall, are a vast number of intermediate devices that must exist to make our phone conversation occur.

## Slide 6: Anatomy of a Local Office Phone Call
Onhook
Means that the phone handset is not lifted off the phone.
The PBX (Private Branch Exchange) provides power and potential across each subscriber loop to monitor the activity and power of each phone.
When the phone is onhook, there is no current flow through the subscriber loop.

## Slide 7: Anatomy of a Local Office Phone Call
Offhook – This refers to the state when a person lifts the phone handset
A switch hook within the phone closes and current flows through the subscriber loop.
The current flow tells the PBX that someone wishes to place a call.

## Slide 8: Anatomy of a Local Office Phone Call
Dial Tone
At this point, the PBX: searches for an unused dial register to store the dialed phone number digits then sends a dial tone through the subscriber loop to offhook phone.
The caller now hears the tone and dials the digit
These digits are sent over the subscriber loop to the PBX dial register.

## Slide 9: Anatomy of a Local Office Phone Call
Ringing Voltage
The PBX looks in its routing table and recognizes that extension eg. 7201, is a local number and exist on another subscriber loop.
The PBX sends a ringing voltage across the subscriber loop to ring the bell within receiver's phone.

## Slide 10: Anatomy of a Local Office Phone Call
Call Completion
Once the person picks up the phone handset, current flows through the subscriber loop and the circuit is complete for the call.
Both can begin talking and their speech is carried over the subscriber loop as an electric signal.

## Slide 11: Components of the Phone System

## Slide 12: The Phone
The phone is an analog device that carries our speech as an electric signal
The handset contains a receiver, transmitter, and hybrid.

## Slide 13: The Phone
Receiver and Transmitter
The handset houses the earpiece or receiver and the mouthpiece or transmitter.
We speak into the mouthpiece and our speech is transmitted over a pair of wires.
We listen through the earpiece or receiver and receive sound over another pair of wires. In total, four wires make up the handset.
Hybrid
The handset also contains a device known as the hybrid.
The phone connects to the PBX using a dedicated pair of wires, the subscriber loop.
The phone receiver/transmitter, however, has four wires. In order to interface between the receiver/transmitter that has four wires and the PBX which uses two-wire, a hybrid is needed.

## Slide 14: Switch Hook
The switch hook is located directly below the handset.
When you lift the handset, the switch hook closes and current flows through the phone. The phone is offhook.
The PBX supplies power to operate the phone.
When you replace the handset, the switch hook opens and current ceases to flow through the phone. The phone is onhook.

## Slide 15: Rotary and Pushbutton Dialer
The dialer is what you use to enter in the phone number you wish to call.
In rotary dialing, you spin the dial to send a digit.
For pushbutton phones, you press buttons which generate a unique combination of tone (called DTMF) to represents each digit.

## Slide 16: The Ringer
When a PBX wants to alert a remote phone of an inbound call, it rings the remote phone by sending ringing voltage down the subscriber loop.
The ringing voltage causes an armature within the phone to pivot.
The armature in turn drives a hammer against a bell, which causes ringing.

## Slide 17: PBX
The Private Branch Exchange (PBX) or switch provides many functions.
It interfaces with phones and provides power to operate and ring the phone.
It also interfaces with other PBXs or to other devices. The interface with the phone is called subscriber side and the interface with PBXs is called the trunk side.

## Slide 18: The PBX

## Slide 19: The PBX

## Slide 20: The PBX

## Slide 21: The Subscriber Loop
The subscriber loop is a dedicated pair of wires that connect the phone to the PBX.
Each phone connected to the PBX has its own subscriber loop.
The subscriber loop consists of two wires known as, Tip and Ring.
The Ring lead connects to the negative side of the battery; the Tip lead connects to ground.
When the circuit is complete, current flows.

## Slide 22: The Trunk Line
Trunk lines connect one PBX to another PBX, or a trunk line can connect the PBX to the outside world, the public phone network.
There can be many trunk lines between two PBXs and these trunk lines are usually shared.
The number of trunk lines available will depend on the number of phones connected to each PBX.
Trunk lines are shared because it is assumed that the phone users will not all simultaneously try to make a call at the same time.
This means that when a call is made, the PBX seizes and uses one trunk line and releases it when the call ends
There are two types of trunk lines, two-wire and four-wire.

## Slide 23: Two Wire Circuits
Two-wire trunk lines are usually used to connect PBXs at distances of up to several thousand feet.
The exact distance between two PBXs will depend on the thickness or gauge of the wire used.
The thicker the gauge, the longer the distance. However, as distance increases the signal quality decreases until the receiver cannot recognize the signal.
In this situation, amplifiers are needed to amplify the signal.
Since amplifiers work in only one direction, the voice is separated into different paths: one for transmit and one for receive.

## Slide 24: Four-Wire Circuits
Four wire trunk lines are used for most high-volume, long distance lines.
A four-wire phone line circuit uses two wires for the transmit path and two wires for the receive path.
Voice and signals are transmitted on the Tip and Ring and received on the Tip1 and Ring1.
If a PBX connects to a four-wire circuit, a hybrid is needed.
The phone connects to the PBX over the two-wire subscriber loop and in order to interface with the four wire trunk line, the PBX uses a hybrid to provide the conversion

## Slide 25: Four Wire Circuits

## Slide 26: Types of Trunk Lines
There are many types of trunk lines. Some can support one way or two way calling, while other trunk lines connect private switches or connect private and public networks.
Some of the common trunk lines are:
Tie Trunks
Tie trunks connect one PBX to another PBX. Tie trunk are either two-wire or four-wire.
Central Office (CO) Trunk
A CO trunk connects the PBX to a local Central Office (CO). The local CO is part of the local phone company. This type of trunk line allows calls to go from a private network to a public network.
Foreign Exchange Station (FXS) Trunk
A typical FXS trunk consists of a subscriber trunk connected directly to a distant CO or a PBX. This service can be leased to avoid long distance charges to a distant CO. The subscriber dials a local exchange number. FXS trunks provide the convenience of a seven-digit number plus service to a distant location at a reduced cost.

## Slide 27: Types of Trunk Lines
Direct Inward Dialing (DID)
Direct Inward Dialing (DID) trunks allow a caller to dial into a PBX directly to a phone or a group of phones without operator intervention. DID typically uses two-wire trunks. In DID, an outside caller dials the number of the desired phone extension, which the connecting CO passes to the PBX.
Direct Outward Dialing (DOD)
With DOD, the extension phone user automatically accesses the local CO without operator intervention. You typically dial “9” and then the outside number.
Wide Area Phone Services (WATS)
Inward WATS and Outward WATS let users either receive or originate long distance calls and have them billed at a bulk rate rather than individually. Inward WATS calls are billed to the called number; outward WATS are billed to the calling party.

## Slide 28: Remote Phone Call

## Slide 29: Signaling
Signaling is important because it is how phone system components communicate and exchange information. For example, in a remote phone call after a PBX seizes the trunk, it sends a setup request message to the other PBX. This is one example of signaling.
Another example of signaling is the dial tone that we hear when we pick up the phone. This is a signal to the phone and the user that the PBX is ready to receive dialled numbers.
Dialling numbers on a phone keypad is another example of signaling.

## Slide 30: Signaling Types
There are three signaling types and each provide particular information about a voice call:

## Slide 31: Address Signaling
Address signaling is how the phone system obtains, transfers, controls, and directs information through the phone system.
You can think of address signaling as the phone numbering system that identifies each phone in a voice network.
All PBXs, Central Offices, or switches will use address signaling to determine how to establish a call to the correct destination. This is called switching the call.

## Slide 32: Address Signaling Cont.
There are two types of address signaling methods:
  Dial pulse. This is associated with rotary dial phones.
  Dual Tone Multifrequency (DTMF) signaling, most often supported on a pushbutton phone.
With dial pulse signaling, digits are sent over the subscriber loop as pulses.
On a rotary phone, when you choose a digit and turn the dial, a spring winds.
When the dial is released, the spring rotates the dial back to its original position, during which time a cam-driven switch opens and closes the loop.
The number of consecutive openings and closings represents the dialed digit.

## Slide 33: Dual Tone Multifrequency
Many phones use tones instead of pulses to send the digits to the PBX.
The keypad has 12 keys, each key or number has a pair of tones: a low frequency tone and a high frequency tone, hence the name Dual Tone Multifrequency (DTMF).
For each row of keys, there are individual low frequency tones.
A different high frequency tone represents each column.

## Slide 34: Information Signaling
Informational signals are generated by the PBX or switch to tell the user about the call’s progress.
There are different types of informational signals; the common types include:
busy signal
fast busy
dial tone
ring back

## Slide 35: Information Signaling Types

## Slide 36: Supervisory Signal
Supervisory signaling monitors the status of a line or trunk, which is either idle (onhook) or active (offhook).
Supervisory signaling types include the following:
  Loopstart
  Ground Start
  E&M

## Slide 37: Loopstart
Loopstart is used primarily on local subscriber loops between a phone and a PBX with two-wire interfaces.
Loopstart refers to the fact that when the phone handset is lifted or offhook, the switch hook is closed and a loop current flows

## Slide 38: Ground start
Ground start signaling is used primarily for trunk line supervisory signaling between a PBX and a PSTN with two-wire interfaces.
Ground start signaling first checks or handshakes with the PSTN or CO to determine if the trunk line is free.
In doing so, ground start signaling avoid glare where both ends attempt to seize the trunk simultaneously.

## Slide 39: E&M Signaling
E&M signaling is a type of supervisory signaling that is commonly used between PBXs.
E&M supervisory signaling differs from loopstart and ground start signaling in that it uses separate paths for voice and signaling, instead of superimposing both voice and signaling on the same wire.